## Slide 1: Generator Wire Boot Install
August 2024

## Slide 2
Undo latches on hood

## Slide 3
Open hood to get to generator from above.

## Slide 4
Remove 4 bolts from black cover on generator(2 in front and two in back) with a 5/16 wrench.

## Slide 5
Remove 4 screws holding on breaker cover.

## Slide 6
Slide breaker out front under cover to access wiring, and remove wires.(7/16 wrench)

## Slide 7
Slide boots on to wires and reinstall wires. Then slide boots up over stud and nut. Reinstall breaker and cover. Then reinstall black cover.